## Slide 1
Fernando Comerón
With thanks to Paul Vreeswijk and the team who implemented the RRM at the VLT

## Slide 2: The ESO Very Large Telescope
4 Unit Telescopes, each 8.2m diameter, on Cerro Paranal (Chile), at 2635m over sea level
The telescopes can be connected to form a near-infrared interferometer, with baselines of up to 120m, also using three 1.8m Auxiliary Telescopes
In operations since 1999
Currently 11 instruments, plus 2 interferometry instruments, covering a broad range of wavelengths, resolutions, and techniques
3 more VLT instruments under construction

## Slide 3: Why a Rapid Response Mode at the VLT?
Great light collecting power: high S/N snapshots of quickly varying phenomena make it possible to study fast, faint transients in great detail
Wide range of instrumentation available: imaging, long-slit and integral field spectroscopy, polarimetry, adaptive optics, high time resolution… both in the visible and near-infrared
Rapid Response Mode offered since April 2004. Currently available at 6 instruments (FORS2, ISAAC, UVES, SINFONI, X-SHOOTER, HAWK-I)
Used thus far for FORS2 (and formerly FORS1), ISAAC, UVES, X-SHOOTER
But the VLT was not designed to be a robotic telescope…

## Slide 4: The VLT operations model
Strongly based on flexible scheduling: most of the time (~70%) devoted to Service Mode observations, with user-specified constraints
Short-term scheduling based on prevailing conditions, user-specified constraints, relative priorities among programmes, degree of completion, time criticality, instrument in use, optimization of the share of calibrations…
Minor fraction (~30%) devoted to Visitor Mode, when real-time decisions based on science criteria are expected (also to keep a strong link between the observatory and the community)
Target-of-Opportuntiy observations can be easily accommodated, non-disruptively, in the Service Mode schedule
Rapid Response observations a bit more challenging, but also feasible…

## Slide 5: How it works
A generic proposal is submitted, selected on scientific grounds
Phase 2: generic Observation Blocks (OBs, logical units describing an observation) are submitted to ESO in advance of the trigger
  RRM OBs contain instrument setup and exposure parameters, but not coordinates
Trigger signal is an ASCII file submitted via ftp to a server in Garching, automatically checked every few seconds by Paranal
  Name indicates instrument and OB to be executed
  Content is just the coordinates
Upon reception, the requested OB is completed (coordinates inserted) and sent for execution
E-mail sent simultaneously to Paranal, including link to finding chart

## Slide 6: How it works
Executability checks performed immediately (target observability, instrument availability, distance to the Moon…)
Ultimate decision on execution is on telescope operator
The telescope can be observing the event within 6 minutes of the trigger arrival

## Slide 7: How it works
Externally generated alert
Alert processing system
Automatically completed OB
trigger
alert
observation request
Operators decision
OK to proceed
Observation
data transfer
Data retrieval

## Slide 8: Some policy issues
RRM have overriding status over any observation currently being completed (other than strictly time-critical ones)
Requested instrument must be in operation at the time of the trigger: no change of focus allowed
RRM triggers accepted up to 4 hours after the event
Follow-up observations after first OB are handled as normal Target-of-Opportunity
For Gamma-Ray Burst (GRB) RRM observations, data are made immediately available to all teams having approved RRM GRB programmes
All data are public through the ESO Archive after one year
Time lost to RRM in Visitor Mode is compensated in Service.

## Slide 9: Usage and performance
14 programmes have made use of RRM observations thus far
Triggered 39 times (as of 17 February 2011)
53h of integration time spent on RRM observations
28 papers including reference to observations made in this mode

## Slide 10: UVES GRB afterglow sample
GRB | ΔT (hh:mm) | z | exptime (hours) | log NHI | [X/H]
020813 | 20:48 | 1.255 | 2.1 |  | 
021004 | 13:31 | 2.329 | 2.0 | 19.0 | 
050730 | 04:09 | 3.969 | 1.7 | 22.10 | -2.18
050820 | 00:34 | 2.615 | 1.7 | 21.05 | -0.39
050922C | 03:47 | 2.199 | 1.7 | 21.55 | -1.82
060418 | 00:10 | 1.490 | 2.6 |  | 
060607 | 00:08 | 3.075 | 3.3 | 17.20 | 
071031 | 00:09 | 2.692 | 2.6 | 22.15 | -1.73
080310 | 00:13 | 2.427 | 1.3 | 18.80 | -1.39
080319B | 00:09 | 0.937 | 2.1 |  | 
080330 | 01:32 | 1.51 | 2.3 |  | 
080413 | 03:42 | 2.435 | 2.3 | 21.85 | -1.60
080804 | 00:50 | 2.205 | 1.3 |  | 
081008 | 04:30 | 1.967 | 1.1 |  | 
081029 | 00:23 | 3.848 | 0.5 |  | 
Programs by Vreeswijk et al., Fiore/D’Elia et al.

## Slide 11: Some highlights
Gamma-Ray Burst (GRB) afterglow photometric and spectroscopic follow-up
Investigation of the intervening intergalactic medium (dust content, metallicity, reionization epoch) along the line of sight to distant GRBs
Investigation of the interstellar medium surrounding the GRB (ionization, dynamics)
GRB/Supernova connection
User only for GRB thus far, but potential goes beyond GRBs (one program currently accepted for RRM observations of giant stellar flares)

## Slide 12: Absorption-line variability: probing the interstellar medium near GRBs
Metastable and fine-structure levels of FeII, NiII at high z detected in absorption against GRBs
UV pumping caused by the GRB followed by fluorescence reproduces model expectations; collisional excitation and direct excitation by infrared photons are discarded.
GRB distance to absorbing clouds can be determined from models; from tens of pc to kiloparsecs (intervening material ionized by the GRB)
GRB spectral slope and UV flux irradiating the cloud are determined too
GRB 060418 from Vreeswijk et al. 2007, A&A 468, 83

## Slide 13: The future
A fast connection between Paranal and Europe will allow near-real time interaction, both ways, between an observer located (nearly) anywhere and the observatory
EVALSO is a pilot project, funded by the European Union’s Framework Program 7, to build a fiber link between Paranal and Cerro Armazones and the Chilean backbone near Antofagasta
Installation completed in November 2010, integration in operations in 2011.
EVALSO will provide Gbps capacity between the observatories and Europe

## Slide 14: The future
The European Extremely Large Telescope (E-ELT) will be a fully adaptive telescope, equipped to address a wide range of astrophysical and cosmological problems
Rapid Response Mode can also be implemented at the E-ELT: diffraction-limited imaging and spectroscopy with a 40m-class telescope
Nothing in the E-ELT design precludes its implementation: fast response time (<20 min after trigger is received) is expected to be possible
Operations expected to begin around 2020

## Slide 15: Concluding remarks
The operations model of large telescopes can accommodate a robotic-like mode for fast follow-up of transients
Enhanced possibilities opened up by remote real-time interaction
New science is possible by operating large telescopes in this mode –and it is happening already now